## Slide 1
A team can have up to 4 members including the team leader. Add rows if necessary.
Team Details
Team Name:
SR. NO
ROLE
NAME
ACADEMIC YEAR
1
Team Leader
2
Member 1
3
Member 2
COLLEGE NAME
TEAM LEADER CONTACT NUMBER
TEAM LEADER EMAIL ADDRESS
Signal Sense
Harini Muthurengan
2
Sofiya.S
2
2
M Thasneem Fathima
B. S. Abdur Rahman Crescent Institute Of Science And Technology
+91 9344472644
harinimuthurengan@gmail.com

## Slide 2
Problem Statement Addressed
Applied Materials – Drift-Sense: Sub-Pixel Pattern Matching & Mechatronic Stage Drift Compensation for SEM Wafer Metrology
DESCRIPTION / DETAILS
  Context: Automated CD-SEM tools must precisely inspect sub-10nm semiconductor features across repetitive wafer dies.
  Stage Drift: Physical stage translation (), chuck rotation (), and optical scaling shift target features off-center.
  SEM Noise: Severe Poisson shot noise, beam astigmatism blur, and charging scanlines degrade pattern visibility.
  Lattice Ambiguity: Repetitive DRAM/FinFET arrays produce identical correlation peaks, causing false pattern locks.
  Significance: Localization errors cause false defect calls and wafer scrap, making sub-pixel precision vital for fab yield.

## Slide 3
Idea Description - Describe your Idea/Solution/Prototype
Provide a brief summary of your idea, including the key concept and approach. Provide a brief overview of your solution and how it addresses the problem statement.
KEY CONCEPT & APPROACH
SOLUTION OVERVIEW
• Complete Suite: Drift-Sense integrates a zero-GPU sub-pixel localization engine with a real-time inspection dashboard.
• Synthetic Physics Engine: Procedurally simulates DRAM/FinFET layouts with Poisson shot noise, charging scanlines, and astigmatism.
• Robust to Distortions: Reliably overcomes stage drift ( ), chuck rotation ( ), and periodic lattice ambiguity.
• Proven Accuracy: Achieves 96.67% pass rate ( ) and 90.00% sub-pixel precision ( ) across 30 test pairs.
• Fab-Ready Speed: Executes in ~1.26s on standard CPU, preventing false CD metrology errors and wafer scrap.
  Scale & Rotation Sweep: Downscales the reference template to and tests angles ( ) to correct geometric misalignment.
  Robust NCC Matching: Uses Normalized Cross-Correlation to find candidate match locations despite severe imaging noise.
  Center-Bias Prior: Resolves periodic DRAM/FinFET lattice ambiguity by favoring the nominal landing area.
  Sub-Pixel Peak Fitting: Employs 2D parabolic interpolation to calculate precise continuous coordinates ( ).
  Fast & Deterministic: Achieves sub-pixel accuracy in ~1.26s on standard CPU without training data or GPUs.

## Slide 4
Proposed Solution - Describe your Idea/Solution/Prototype
Describe your idea in detail. Include the methodology, technologies involved, and how it addresses the chosen problem statement.
SOLUTION DETAILS
• Multi-Scale Geometric Alignment: Downsamples the reference template (~ ) across affine rotation sweeps ( ) to correct stage skew.
• Robust ZNCC Matching: Evaluates Zero-Mean Normalized Cross-Correlation to deliver illumination- and contrast-invariant candidate matching.
• Gaussian Center-Bias Prior: Applies a spatial distance penalty to mathematically resolve periodic lattice ambiguity in dense DRAM arrays.
• 2D Parabolic Peak Fitting: Employs quadratic Taylor interpolation around correlation peaks to calculate continuous sub-pixel coordinates ( ).
• CPU-Optimized Software Stack: Implemented in Python/NumPy/OpenCV & TypeScript/React for real-time inference (~1.26s) without requiring GPU hardware.

## Slide 5
Innovation and Uniqueness
Highlight what makes your idea unique or innovative compared to existing solutions.
KEY INNOVATION
• Physics-Informed Mechatronic Prior: Integrates stage landing probability to mathematically eliminate false locks in periodic DRAM lattices.
• Continuous 2D Sub-Pixel Interpolation: Uses parabolic Taylor expansion on correlation peaks to achieve registration accuracy.
• Synthetic SEM Physics Engine: Procedurally emulates Poisson shot noise, dielectric charging scanlines, and astigmatism without beam-time.
• Multi-Scale Affine Normalization: Geometrically aligns reference templates to search fields across continuous rotations ( ).
• Zero-Training Deterministic Logic: Completely explainable mathematical pipeline with zero hallucinations or out-of-distribution risks.
COMPETITIVE ADVANTAGE
• No GPU Hardware Required: Fully CPU-optimized, easily deploying directly onto existing industrial SEM embedded controllers.
• Zero Data Annotation Cost: Eliminates the need for thousands of manually labeled SEM images required by Deep Learning/CNNs.
• Ultra-Fast Throughput: Delivers ~1.26s inference per image pair, preventing wafer inspection bottlenecks.
• Proven High Accuracy: Achieved 96.67% pass rate ( ) and 90.00% sub-pixel accuracy ( ) in 30-pair test suite.
• Interactive Metrology Suite: Features a real-time web dashboard for parameter tuning, physics visualization, and instant batch benchmarking.

## Slide 6
Impact and Benefits
Explain how your solution will make an impact, such as improving performance, reducing costs, increasing efficiency, or solving other challenges.
Primary Impact
• Prevents High-Cost Wafer Scrap: Eliminates false Critical Dimension (CD) measurement errors and unnecessary wafer rejection in High-Volume Manufacturing (HVM).
• Maximizes Fab Tool Throughput: Removes manual inspection recovery and re-scan cycles with fast, automated pattern localization.
• Enables Sub-10nm Process Control: Provides deterministic sub-nanometer registration essential for next-gen FinFET and dense DRAM yield.
• Zero-Cost Integration: Runs directly on legacy fab tool controller CPUs without expensive GPU hardware upgrades.
• Reduces SEM Beam Damage: Fast single-shot matching minimizes electron-beam exposure time on delicate photoresists.
Quantifiable Outcomes
• 96.67% Overall Pass Rate: Successfully localized targets within strict metrology limits () across 30 test pairs.
• 90.00% Sub-Pixel Precision: Achieved high-fidelity registration error
across severe noise conditions.
• ~1.26s Execution Time: Delivers fast CPU inference per image
pair without GPU acceleration.
• 100% Training & Label Free: $0 spent on dataset annotation, model training runs, or GPU cloud instances.
• Robust to Drift & Skew Completely suppresses false locks in repetitive periodic lattices.

## Slide 7
Technology & Feasibility/Methodology Used
Describe the technologies, methodologies, or tools you plan to use to implement your idea.
IMPLEMENTATION STRATEGY
  Algorithms : Multi-scale affine ZNCC matching, Gaussian center-bias prior, and 2D parabolic Taylor sub-pixel interpolation.
  Core Engine : Pure Python with NumPy and OpenCV for deterministic, vector-accelerated matrix operations.
  Interactive Metrology UI : React 18, TypeScript, Tailwind CSS, Lucide Icons, and Canvas API for live inspection.
  Synthetic SEM Simulator : Procedural DRAM/FinFET generator modeling Poisson noise, astigmatism blur, and charging scanlines.
  Fab Feasibility : Ultra-low CPU compute footprint (~1.26s/pair) directly compatible with existing fab tool controllers without GPUs.
Software Architecture
Hardware Components
Development Tools
• Modular Python metrology pipeline + REST / WebSocket API + Modern React/TypeScript frontend dashboard.
• Standard x86_64 Industrial Workstation / IPC (Zero GPU required; minimal memory and compute footprint).
• Python 3.10+, OpenCV, NumPy, SciPy, Vite, Node.js, Tailwind CSS, Git.

## Slide 8
GitHub & Video Link
GitHub Repository
https://github.com/Harini7878/SEMICON-India-2026
Prototype / Simulation Video
https://canva.link/op815z0vqmlav89

## Slide 9
Research and References
Research Background & Methodology
Briefly describe the research foundation or scientific principles supporting your idea.
• Statistical Normalized Cross-Correlation (NCC): Leverages ZNCC theory for contrast- and illumination-invariant template matching under low electron dose.
• Gaussian Spatial Prior Theory: Models mechanical stage landing error as a normal distribution to suppress false peaks in periodic DRAM arrays.
• 2D Taylor Surface Interpolation: Fits continuous quadratic paraboloids over discrete discrete correlation maxima to break the 1-pixel Nyquist barrier.
• SEM Electron Interaction Physics: Grounds validation on Monte Carlo/Poisson electron scattering models, astigmatism blur, and scanline charging physics.
• Deterministic Non-Parametric Framework: Bypasses neural hallucination vulnerabilities, guaranteeing mathematical reproducibility for metrology certification.
References & Citations
List key papers, articles, or data sources.
• Ref 1: Lewis, J. P. – "Fast Normalized Cross-Correlation," Vision Interface, Proc. Canadian Image Processing and Pattern Recognition Society.
• Ref 2: Postek, M. T. & Vladár, A. E. – "Critical Dimension SEM Metrology and Modeling in Semiconductor Manufacturing," SPIE Advanced Lithography.
• Ref 3: Applied Materials Metrology Benchmark – "Sub-Pixel Pattern Localization and Stage Drift Compensation under Low-Dose SEM," Hackathon Problem Track.